## Slide 1: Maze Router
Ismael Elsharkawi
Mahmoud Elsayed
Ahmed Ehab Hamouda

## Slide 2: Outline
Division of the work
The Input Parser
The A* Algorithm and Routing using A*
The LEF and DEF Parsers
Run Examples
Complexity Analysis

## Slide 3: Division of the work
Ismael Elsharkawi
Built the Input Parser
Worked on some modifications in the A* Algorithm in python
Made the PNG drawer
Made the DEF and LEF parsers in python
Mahmoud Ahmed
Built most of the A* algorithm and its classes including the pins, the nodes.
Made most of the routing algorithm using the A* algorithm
Mohamed Hamouda
Worked on the A* algorithm in C++ before switching to python, then worked on it with python.
Fixed some issues in the A* algorithm

## Slide 4: Design tradeoffs
Due to the limited time of the project, the router was developed using python
Python:
  Easier implementation
  Slower runtime
C/C++:
  More complex implementation
  Faster runtime

## Slide 5: Input Parser
A class called InputParser was created.
It extracts the input pins locations for each net using regular expressions and saves them in classes of type Pin, there is a vector of pins that represents the net, that vector is pushed into the nets vector that is an attribute of the class InputParser.
PinsGrid is a python dictionary that takes a tuple of three elements representing the layer, y-coordinate, x-coordinate.

## Slide 6: A* Algorithm
The A* algorithm depends on a priority queue called open_list.
At each position we are standing at, we calculate a function f, where f = g + h. g is the cost from the starting position until the current location, h is the heuristic function, that is the estimated cost of reaching the target.
Choose the position with the least value of f as the new position, remove it from the open_list and add it to the closed_list, we continue doing that until we reach any of the targets.
Create the children for each node and calculate the cost function for it and mark this node as invalid on the grid.

## Slide 7: A* Algorithm: cost
The g function is calculated for even layers as :
The function g is calculated for odd layers as:

## Slide 8: LEF and DEF formats parsing
We parse both the LEF and the DEF to make the input list that the input parser expects
The components, nets, pins, rows, tracks, etc. are saved in classes.
We get the location of each macro from the DEF file, then we get the relative location of each pin from the LEF file, then we get the nets from the DEF file again, then we get the location of the global pins.

## Slide 9: Example Runs
This is the input file
The output png images are shown in the following slides, one layer in each slide.
This is the output of the sample

## Slide 10: Layer 1

## Slide 11: Layer 2

## Slide 12: Layer 3

## Slide 13: Layer 4

## Slide 14: Performance
Runtime

## Slide 15: Example Runs
This is the input file
The output png images are shown in the following slides, one layer in each slide.
This is path of the output of the sample

## Slide 16: Layer 1

## Slide 17: Layer 2

## Slide 18: Layer 3

## Slide 19: Performance
Runtime

## Slide 20: Example Runs
This is the input file
The output png images are shown in the following slides, one layer in each slide.
This is path of the output of the sample

## Slide 21: Layer 1

## Slide 22: Layer 2

## Slide 23: Performance
Runtime

## Slide 24: Example Runs
This is the input file
The output png images are shown in the following slides, one layer in each slide.
This is path of the output of the sample

## Slide 25: Layer 1

## Slide 26: Layer 2

## Slide 27: Layer 3

## Slide 28: Layer 4

## Slide 29: Performance
Runtime

## Slide 30: Example Runs
This is the input file
The output png images are shown in the following slides, one layer in each slide.
This is path of the output of the sample

## Slide 31: Layer 1

## Slide 32: Layer 2

## Slide 33: Performance
Runtime

## Slide 34: Limitation
Python runtime slows down the performance
Memory complexity is high

## Slide 35: Future improvements
Support all the DEF/LEF format information
Implement Rip-up Reroute
Check for the possibility of threading the routing to reduce time